## Slide 1: Seeing and Measuring at the Nanoscale
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Need to start by clarifying what we mean by “seeing”
It generally means collecting information point by point
To do this, the key is to perform some sort of triangulation:
Line 1:
Line 2:
X?

## Slide 2: But when I look at things I don’t always triangulate!
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
When things are close, you triangulate by using “binocular vision”
When things are far, you triangulate by inferring surfaces Huh?
You construct a second triangulation line by inferring which surface the point is on
(Along with the relative distances of different surfaces)
Line 1:
Line 2:
X?
Eye:

## Slide 3: How is that relevant to seeing at the nanoscale?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
It's relevant because, at the nanoscale, seeing gets a lot harder
And it requires a lot of complex and expensive engineering
So you need to reduce “seeing” to its barest essentials
The essential for triangulation is that you have a well defined PROBE and SIGNAL:
Probe (stimulus):
Signal (response):
X?
Line 1:
Line 2:
Then for info at multiple points: SCAN!

## Slide 4: Do BOTH probe & sensor have to be direction sensitive? No!
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Non-directional source: Non-directional sensor:
X?
Line 1:
Line 2:
X?
Line 2:
Line 1:
So on surfaces, you can greatly simplify either source or sensor!

## Slide 5: But this still seems to rule out use of light at the nanoscale
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Because we still need one thing (source OR sensor) to be nano directional
And we know, from lecture 2, that light will not stay confined into nano beam < l wide:
“Diffraction limited focusing”
But there is a trick: Don’t give light enough room to spread out:
But how do we then see around that bulky aperture?
Use drawn down optical glass fiber:
Also works in reverse to sense light for sub l point
X?
Nanoscale
Aperture

## Slide 6: NSOM: Near-Field Scanning Optical Microscopy
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
From above: Sub l wide light from end of fiber
To below: Optics and various light detectors
With exact position determined by:
Surface + X-Y Position of Fiber’s End
Drawn down glass fiber
Metal mirror coating to funnel light

## Slide 7: The 2014 Chemistry Nobel recognized another end run on diffraction:
To Eric Betzig for the Photoactivated Localization Microscope (PALM)
Working in sister department of mine while we were at Bell Labs
Problem: We can put photochemical tags at specific locations in cells & molecules
Incoming light can cause tag to emit light of different color (fluoresce)
But light emitted from nanoscopic tag then blurs due to diffraction!
Solution: Light from single tag will radiate out in precisely circular waves
Set up conditions so that only a few distant tags radiate at one time
Then, their growing circular blobs of light won't overlap (confusing image)
Figure out the center of each circular light blob (via computer analysis)
=> Precise position of each tag
Subsequent images => positions of other tags => map of cell / molecule

## Slide 8: Or as depicted by the Nobel organization:
http://www.nobelprize.org/nobel_prizes/chemistry/laureates/2014/popular-chemistryprize2014.pdf

## Slide 9: Scanning Probe Microsopies (SPMs)
But NSOM & PALM are ~ limit of all light seeing. Other ways of nanosize things? Yes:
Derived from inventions of Bennig & Rohrer, and Quate
Scanning Tunneling: Electrons tunnel between atomically sharp probe and conducting sample
Atomic Force: Nanometer sharp probe rubs or taps along surface of any sample
"DI Dimension 3100" SPM capable of both AFM and STM operation:
Complete detailed description of instrument's operation and piezoelectric core at:
https://WeCanFigureThisOut.org/VL/SPM_operation.htm
https://WeCanFigureThisOut.org/VL/SPM_piezoelectric.htm

## Slide 10: OR the units we've used in this class's lab:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Nanosurf easyScan2 Atomic Force Microscope:
Complete description at: https://WeCanFigureThisOut.org/VL/easyScan_AFM.htm
Nanosurf easyScan2 Scanning Tunneling Microscope:
Complete description at: https://WeCanFigureThisOut.org/VL/easyScan_STM.htm

## Slide 11: And SPM's can do more than just measure surface shape:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
STM: Pulls electrons FROM sample → from FILLED electron orbitals OR:
Pushes electrons INTO sample → to EMPTY electron orbitals
=> Energy levels of surface atoms and molecules
Current from STM or AFM tip is also sensitive to sample's local electrical resistance
=> Concentration maps of electrically active impurities in semiconductors
In alternating current modes, STM and AFM tips can be sensitive to capacitance
=> Maps of electrical impurities and their energy levels
Plus:
MANY, MANY other modes that give information on far more than surface shape!

## Slide 12: But probe microscopies have their own limitations:
"A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Ultra-fine probe tips are difficult to make and very easy to damage
So samples need to be almost atomically flat
Meaning SPMs cannot look at a whole lot of interesting samples!
And even with ultra flat samples, nano probes will STILL get damaged!!
Requiring expensive replacement probes & probe mounting schemes
Besides which:
What if want to sense things BELOW surfaces?
What if want to know more than shape (e.g. composition, bonding . . . )?
So it is time to look much farther afield for possible probes and sensors

## Slide 13: Start by identifying the full range of potential probes & signals:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
1) Physical probes (points, needles . . .) 2) Ions / Atoms
3) Electrons 4) Photons
We can design at least (!) one instrument around each of these probes/signals
But that is far too limiting!
Analysis consists of sending something in, and looking at what comes out
STIMULUS AND a RESPONSE
Each of the above probes/signals can serve as the STIMULUS
And almost all of the above probes/signals might be part of the RESPONSE

## Slide 14: So these generate a whole matrix of possibilities:
Ions in & out: Secondary ion mass spectroscopy (SIMS) . . .
Electrons in & out: Scanning Electron Microscopy (SEM),
Transmission Electron Microscopy (TEM),
Auger electron spectroscopy (AES) . . .
Photons in & out: IR spectroscopy (FTIR), Ellipsometry . . .
Photons in / Electrons out: X-ray and UV photoelectron spectroscopy (XPS, UPS, ESCA)
Electrons in / Photons out: Energy Dispersive Analysis of X-rays (EDAX) . . .
And virtually every other combination imaginable!
With even more variations if you switch to different ranges of energy!

## Slide 15: Let's go through stimulus/response possibilities more slowly:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Atoms / Ions: Big and heavy → Not used that much in nanoscience
If we shoot them in, we'll alter (likely destroy) the structure
If they are coming out, we must have already torn apart the nanostructure
Electrons: Small, light, charged
Small and light → Good news: They generally cause minimal damage
Charge → Good news & bad news:
Easy to steer and focus - Just need electric field between metal plates
But don't play well with insulating samples
Shoot them in → Insulator charges up negative
If with more than ~10 eV → kicks out "secondary electrons"
Charging → Electric fields → Complicates counting and measurement of energies

## Slide 16: And size of electron or electron-beam can get tricky:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Individual electrons have variable size defined by Quantum Mechanical wavelength:
l de Broglie = Plank’s constant / Electron’s momentum = h / √(2 m E)
And a small BEAM of multiple electrons will spontaneously get wider:
Electrons repel one another!
Solution? Fast high energy electrons are smaller
Fast high energy electron beams stay narrow over longer distances
But there is a downside: High energy → Long penetration
Electrons in: Stimulate signals from large volumes and depths
Electrons out: Collected from large volumes and depths

## Slide 17: Approximate numbers?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
For electrons entering or leaving solid matter:
Limit to resolution:
1) Minimum e-beam width
Electron Energy Penetration / Escape Depth 2) Electron size (wavelength)
1-5 keV tenths of nanometers Microns to 10's of nanometers 1
10-50 keV nanometers 1-10 nanometer 1
100 -1000 keV tenths of MICRONS tenths - hundredths of nanometers 2
Or schematically showing incoming + outgoing beams, and volume probed:
Low electron energy: High electron energy:

## Slide 18: Opportunity for narrow high energy electron beams:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Beams can penetrate far but are very narrow
Use to sense things that are essentially in columns along the incoming beam direction:
Scan beam across sample
Narrow beam distinguishes between different columns
Where to find such configurations in nature? Crystals!
= Basis for Transmission electron Microscopy (TEM)
"Atomic resolution" image from my research on growth of GeSi on Si

## Slide 19: Transmission electron microscopy:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
But TEM only has pseudo atomic resolution = End on views of atom COLUMNS
While useful for semiconductor crystals - Not that useful for 3D nanostructures!
Left: www.biotech.unl.edu/microscopy/TEM.htm
Right: www.uiowa.edu/~cemrf/methodology/tem/index2.htm
Lenses
Lenses
e-source
sample
image

## Slide 20: A way of using the fat low energy electrons?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Stimulate using narrow high E electrons:
Yes, in combination with skinny high energy electrons / electron beams
Most popular alternative is to use high E stimulus beam + low E response beam
Sense only low E electrons emerging from ~ surface
Intersection of stimulus and response volumes = Small 3D volume produces the data!
+ =>

## Slide 21: Scanning Electron Microscopy (SEM):
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
(From https://WeCanFigureThisOut.org/VL/SEM.htm)
Incoming electrons ~ 5 keV => moderately narrow / moderately deep penetration
Outgoing electrons ~ few eV or less => liberated from top couple of atomic layers
But X-rays that are ALSO stimulated and give information on sample composition
This requires add-on sensor called "EDAX" - Energy dispersive analysis of X-rays

## Slide 22: What about photons used ONLY for probe or signal?
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
GOOD NEWS: They cause ~ no damage (unless very high energy, e.g. UV)
BAD NEWS: They are BIG
Width: Diffraction means we can only focus down to beam ~ one wavelength wide
=> Stimulate / collect signal from areas 1000's of atoms wide (like low E electrons!)
Depth: Photon penetration/escape depends on material and wavelength
METALS: Almost zero penetration/escape depth with highly conductive samples
But also almost zero information out (as beam reflects ~ unchanged)
NON-METALS: Penetration/escape depths = wavelength to many wavelengths
So see cumulative effects of hundreds-thousands of layers

## Slide 23: Thus combine light with another probe or signal
"A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Alternative #1)
Send photons in: Penetrate and stimulate 100's-1000's of atom planes deep
Sense electrons out: Kicked out by photon energy (eV's to keV's)
These electrons can only escape from first few atomic layers!
Alternative #2)
Send electrons in: If limit energies to few keV, can only penetrate few atomic layers
Sense photons out: Those stimulated by the incoming electrons
Either way, only collect information about the first few atomic layers!

## Slide 24: But we need to know more about how photons & electrons interact with atoms:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Goes back to atomic energy levels (electron standing waves in funny box):
E
x
Energy of electron freed from atom and at rest
(defined as E = 0)
Higher atomic energy levels
Those occupied by bonding ("valence") electrons
Lower atomic energy levels
Occupied by "core" electrons oblivious to outside world
- E binding 4
- E binding 1

## Slide 25: Now send in a photon or electron to knock out core electron
Simplest conversion of energy: Assume ALL of incoming energy is absorbed
E out = E in - E binding 3
E = 0
E in
- E binding 3
Core levels (sharp / un-broadened)
Valence levels (broadened)
Core energy levels are unique to each atom and unaffected by bonding:
If you know precise E in can calculate core energy levels from E out
Gives you the chemical identity (and approx. concentration) of atoms probed
Measured over depth of few atom layers because only those electrons can escape

## Slide 26: Different information for different ejected electron energies:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Core electron levels were unaffected by neighboring atoms
Gave unambiguous ID of originating atom - but nothing about what it is bonded to
So use this when you need to know what atoms sample is made of
Valence electron levels ARE changed significantly by neighbors
This blurs the ID of the originating atom - but can give REALLY good bonding info
So use when you know atoms in sample but want to learn their arrangement
Or between these extremes medium electron levels are slightly changed by neighbors
This provides slightly ambiguous ID of originating atoms + some bonding info
How do you select? By choosing energy of INCOMING photon or electron:
keV ejects ALL 10 eV ejects medium Few eV ejects only valence
(use electrons) (use electrons or X-rays) (use UV or visible light)

## Slide 27: Particularly precise and instrumentally simple technique:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Auger Electron Spectroscopy
Involves electrons in + electrons out. But process incorporates a subtle twist:
keV electron knocks core electron out
E in
Core levels
Valence levels
E M
E K
Higher electron drops down, fills vacancy, releasing energy as photon
Shallow electron absorbs photon, acquiring energy to escape out into space
E L
E out = (E L-E K) - E M ≠ f (E in)

## Slide 28: Thus Auger spectrometer identifies atoms very simply:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Can use any old electron source (no need to carefully control incoming energy!)
Can easily measure energy of emitted electrons by how they bend in electric field
Electrons shoot from electron gun at center (orange), into sample (green)
To reach detector (yellow), ejected electrons must negotiate maze (thru cylinder gaps)
For given set of voltages, only electrons of one energy can do this

## Slide 29: Or more schematically:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Three concentric grounded cylinders inside long negative cylinder
Cheap electron gun inside second cylinder shooting at sample
Some electrons emitted from sample pass through cylinder-1 / cylinder-2 gap
Voltage on long outer cylinder selects which bend enough to make through following gap
Where are counted (V then scanned to change electron energy → spectrum)
V
Cylindrical Mirror Analyzer (CMA)
Sample

## Slide 30: Sometime problem in nano-AES analysis: damage
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Incoming electrons ~ keV in energy: Energy/charge can damage nano-samples
So switch to lower energy PHOTON beam to only knock electrons out
Good News: Knocks out “shallow” valence electrons → chemical + bonding info
Bad News: Outgoing energy IS ONCE AGAIN function of incoming energy
No longer using tricky Auger energy exchange process
Just transferring incoming photon energy to outgoing electron
To precisely determine atomic energy levels → Must use extremely well defined Ein
NEED 2 SPECTROMETERS! One to filter incoming photon energy!
One to filter outgoing electron energy

## Slide 31: Instrument's name then depends on photon energy:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Ultraviolet photoelectron spectroscopy (UPS): UV in, very shallow electrons out
X-ray photoelectron spectroscopy (XPS): X-rays in, medium shallow electrons out
XPS (a.k.a. "ESCA" - Electron Spectroscopy
for Chemical Analysis) often preferred:
Medium shallow electrons →
Can still identify atomic source
+ get some bonding info
But instrument is now quite complex:
Electron Gun
Al Anode
Quartz Crystal
Monochromator
Analyzer
Input Lens
This figure (and ones to follow) courtesy of Guy Messenger,
ULVAC-PHI Inc.

## Slide 32: Taking XPS apart piece by piece:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
High energy electron beam → Aluminum Anode
= Common way of producing "K-a" X-rays
But X-rays span energy range - So they are then filtered:
Electron Gun
Al Anode
Quartz Crystal
Monochromator
Periodic atomic structure of Quartz crystal reflects only certain X-ray
l = 0.83386 nm → 1.5867 keV
Mirror is curved to focus those reflected X-rays onto sample:
(Source: ULVAC-PHI)

## Slide 33
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Where focused X-ray beam (pink)
Creates electrons (yellow)
Which are analyzed by passing through electric fields
(Same idea but slightly different geometry than Auger CMA)
Analyzer
Input Lens
X-ray spot size on sample ~ 10 microns (over which area the info is averaged)
But that beam can then be scanned over larger area of sample:
(Source: ULVAC-PHI)

## Slide 34: And now it really gets interesting:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Al X-rays
1) Electron beam raster scans across Al anode
Creates raster scanned
spot of emitted X-rays
Al Anode
2) X-ray beam from changing spot reflects off Quartz crystal at changing angle
Sample
3) Which produces single energy X-ray beam that raster scans across sample
Electron Gun
Quartz Crystal
Monochromator
Analyzer
Input Lens
4) Yielding electrons whose energy is analyzed
(Source: ULVAC-PHI)

## Slide 35: But resulting XPS instrument requires a lot of hardware:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Monochromator
Anode
E-Gun
Vacuum Chamber Configuration
1. Scanning X-ray source
2. Electron energy analyzer
3. Optional C60 sputter ion gun
4. Argon sputter ion gun
5. Sample introduction chamber
6. Five axis automated sample manipulator
7. Optical microscope
8. Optional dual anode x-ray source
9. Optional UV light source for UPS
(Source: ULVAC-PHI)

## Slide 36: A seemingly big problem with all of those spectroscopies:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
What happened to the required triangulations to get precise positions?
It was lost because either probe or response beam was too broad!!!
Yes, but we can partially make up for that:
In addition to telling you what atoms a sample is made of
spectroscopies using valence/near-valence electrons also give bonding
From known bonding, you can begin to construct the overall structure:
Si's are bonded to O, O's is bonded to H . . . .
At least, should work for fairly simple nanostructures
DIFFICULT, yes, but it's how most nanostructures were originally determined!

## Slide 37: OK, but something still seems to be missing!
"A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
I've shown techniques for measuring nano things on surfaces
I've shown how to measure nanoscale composition & bonding of samples
But how do you figure out the structure of very complex nano things?
How were things like THIS figured out
(i.e. DNA & proteins)?
Essential techniques are: X-ray and electron diffraction
Tricky to explain, very difficult to interpret
But, in the right hands, they can be golden

## Slide 38: They exploit wave nature of both X-rays and electrons:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
From lecture 2, every position on a wave acts like a vibrating point
Producing expanding circular waves
When points are in line & in phase, sum of circles => plane wave
Waves from vibrations at one point => vibrations (+ waves) from adjacent points
That’s getting a bit complicated – We need an intuitive example:
Remember my rule that “a wave is wave is a wave”
So imagine loud sound causing bell to ring:

## Slide 39: So watch as wave progresses by one bell:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Pulse of sound: Now past the bell, causing it to ring:
Now imagine a GROUP of DIFFERENTLY SIZED bells
(different size bells = different atoms of a molecule):

## Slide 40: It induces “sympathetic” ringing in those bells:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Result of speaker sending out single pulse of sound a little while ago:
Then apply “principle of superposition” to add separate waves => Scattered wave
Different arrangements / different size bells => Different net scattered wave!

## Slide 41: Challenges with such diffraction techniques:
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
1) Induced “ringing of bells” is likely to be very weak => very weak total signal
Solution: Use regular repetitions of groupings = CRYSTAL of molecules
Getting those complex organic molecules to
crystallize is thus a critical (difficult) first step!
2) INVERSE PROBLEM: Known grouping => Calculation of net diffracted signal
But from measured diffracted signal, can you figure out the grouping?
Sub-question a) Do different groupings produce unique signals?

## Slide 42: Mathcad simulations of wave striking different groupings
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Wave, rotating slowly around, striking three different groupings of bells / atoms:
vs. vs.
Single frame from movie:
Link to full animation embedded in webpage: Seeing at the Nanoscale - Supporting Materials - Simulation

## Slide 43: So subtly different arrangements DO produce unique diffraction!
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Sub-question b) From unique patterns, can you infer responsible arrangements?
There is no well defined mathematical approach for converting pattern to structure
It instead requires first making very good guesses . . . plus a huge amount of work!
Confirmation of this difficulty?
Interpretation of X-ray data to define
this structure => 2006 Nobel Prize
RNA Polymerase (blue) acting on DNA (gold)
(figure from Wikipedia)

## Slide 44: In Summary: "Seeing" at the nanoscale is VERY challenging
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
We seldom obtain easy images as we see them in our daily lives
Instead we are often reduced to feeling our way along nano-point by nano-point
OR
Triangulating & scanning (employing directional sources AND/OR signals)
OR
Inferring structure from spectroscopies that identify atoms & their bonding
OR
Tour de force interpretation of signals such as X-ray or electron diffraction
Nevertheless, now have tremendously detailed knowledge of nano-structures!

## Slide 45: Credits / Acknowledgements
A Hands-on Introduction to Nanoscience: WeCanFigureThisOut.org/NANO/Nano_home.htm
Funding for this class was obtained from the National Science Foundation (under their Nanoscience Undergraduate Education program).
This set of notes was authored by John C. Bean who also created all figures not explicitly credited above.
Copyright John C. Bean
(However, permission is granted for use by individual instructors in non-profit academic institutions)